## Slide 1: LCD Display
Lab 05

## Slide 2: Your Task
Display characters according to the button pressed
A
B
C
…
ABC_

## Slide 3: Grading
Basic: (60%)
  Display the character pressed at the cursor position
Bonus 1: (+10%)
  Implement the `new-line’ key
  Change to the next line if new-line pressed at Line 1
  Scroll the screen if new-line pressed at Line 2
Bonus 2: (+20%)
  Implement the arrow keys (up, down, left, right)
  Move the cursor by the arrow key
  Insert character at the cursor position
Bonus 3: (+20%)
  Catch the signal waveform of sending a command/data using LA

## Slide 4: Schedule
11/9: demo the basic part
11/16: demo the bonus

## Slide 5: General Concepts: Controlling I/O Devices
On-chip vs. off-chip

## Slide 6: Control on-chip peripherals
access control registers with memory-mapped I/O
CPU
memory
disk
USB controller
GPIO
…
System interconnect
Command
Status

## Slide 7: Control off-chip peripherals
Transfer command/data through off-chip buses
Following some protocol (waveform)

## Slide 8: Control the LCD Display
From the hardware perspective

## Slide 9: Signal Interface to the LCD
The application processor sends commands and data through port P3
A command:
  Moving cursor
  Clear screen
  …etc
Data: the ASCII code of the character to display

## Slide 10: Signal interface to the LCD
RS: register select
  0: command
  1: data
E: latch enable
  the LCD latches the command/data at negative edge (10)
D [7:0]
  the 8-bit data/command
  configured 4-bit mode
  send higher portion first

## Slide 11: List of commands
http://www.eeherald.com/section/design-guide/sample_lcd_c_programs.html

## Slide 12: Timing diagram to send command/data
Example: to send command 0x01
clear screen, cursor home
E
RS
D[3:0]
0
0
0
1
time
latch command
Higher-half of
the command
Lower-half of
the command
latch command

## Slide 13: Timing diagram to send command/data
Example: to send data ‘A’=0x41
The LCD prints ‘A’ at the cursor position
E
RS
D[3:0]
1
4
1
1
time
latch data
Higher-half of
the data
Lower-half of
the data
latch data

## Slide 14: How to program the LCD
Demo: LCD_Hello

## Slide 15: Initialize the LCD

## Slide 16: Program to send command/data
Example: to send data ‘A’=0x41
The LCD prints ‘A’ at the cursor position
E
RS
D[3:0]
1
4
1
1
time
Prepare the data
Higher-half of
the data
Lower-half of
the data
Prepare the status word

## Slide 17: Program to send command/data
Example: to send data ‘A’=0x41
The LCD prints ‘A’ at the cursor position
E
RS
D[3:0]
1
4
1
1
time
Send out the data
Higher-half of
the data
Lower-half of
the data
Send out the status word

## Slide 18: Program to send command/data
Example: to send data ‘A’=0x41
The LCD prints ‘A’ at the cursor position
E
RS
D[3:0]
1
4
1
1
time
Prepare the data
Higher-half of
the data
Lower-half of
the data
Prepare the status word

## Slide 19: Program to send command/data
Example: to send data ‘A’=0x41
The LCD prints ‘A’ at the cursor position
E
RS
D[3:0]
1
4
1
1
time
Send out the data
Higher-half of
the data
Lower-half of
the data
Send out the status word

## Slide 20: Program to send command/data
Example: to send data ‘A’=0x41
The LCD prints ‘A’ at the cursor position
E
RS
D[3:0]
1
4
1
1
time
Send out the data
Higher-half of
the data
Lower-half of
the data
Send signal for lower-half