## Slide 1: 8051 Assembly Programming
Lab 01

## Slide 2: Today’s Goal
Guide you to write your first 8051 assembly program
  and perhaps your first assembly program
Your work: write a program to compute
  where A[i], B[i] are integer arrays (8-bit) in 8051’s internal memory

## Slide 3: Overview: the C8051F040 SoC
a system-on-a-chip integrating the processor core, memory, peripheral devices, everything in a computer syste,

## Slide 4: Fundamental: von Neumann model in assembly level

## Slide 5: The Von Neumann Model
D = A+B*C;
E = D+F;
A = A-1;
10
A
20
B
30
C
40
D
50
E
60
F
memory
CPU
PC: program counter

## Slide 6: The Von Neumann Model
D = A+B*C;
E = D+F;
A = A-1;
10
A
20
B
30
C
610
D
50
E
60
F
memory
CPU
PC: program counter
PC

## Slide 7: The Von Neumann Model
D = A+B*C;
E = D+F;
A = A-1;
10
A
20
B
30
C
610
D
670
E
60
F
memory
CPU
PC: program counter
PC

## Slide 8: The Von Neumann Model
D = A+B*C;
E = D+F;
A = A-1;
9
A
20
B
30
C
610
D
670
E
60
F
memory
CPU
PC: program counter
PC

## Slide 9: How a CPU works?
follow the von Neumann model
  step by step
  one instruction per step
but decompose operations into primitive and regular ones
D = A+B*C;
E = D+F;
A = A-1;
load R1, A; //R1 = mem[A];
load R2, B; //R2 = mem[B];
load R3, C; //R3 = mem[C];
mult R4, R2, R3; //R4=R2*R3;
add R5, R1, R4; //R5=R1+R4;
store D, R5; //mem[D] = R5;
load R6, F; //R6 = mem[D];
add R7, R5, R6; //R7 = R5+R6;
store E, R7; //mem[E] = R7;
sub R1, R1, 1; //R1 = R1-1;
store A, R1; //mem[A] = R1;
assembly program

## Slide 10: Question
Q: what’s the major difference between assembly programming and high-level language programming?
A: you have to imagine how hardware works!

## Slide 11: How a CPU works?
from hardware design perspective
the data path:

## Slide 12: How a CPU works?
registers to store variables
registers

## Slide 13: How a CPU works?
function units to perform computation
function units

## Slide 14: How a CPU works?
still follows von Neumann model
A = B+C;
load R1, B; //R1 = mem[B];
load R2, C; //R2 = mem[C];
add R3, R1, R2; //R3 = R1+R2;
store A, R3; //mem[A] = R3;
A
B
C
memory

## Slide 15: How a CPU works?
still follows von Neumann model
A = B+C;
load R1, B; //R1 = mem[B];
load R2, C; //R2 = mem[C];
add R3, R1, R2; //R3 = R1+R2;
store A, R3; //mem[A] = R3;
A
B
C
memory

## Slide 16: How a CPU works?
still follows von Neumann model
A = B+C;
load R1, B; //R1 = mem[B];
load R2, C; //R2 = mem[C];
add R3, R1, R2; //R3 = R1+R2;
store A, R3; //mem[A] = R3;
A
B
C
memory

## Slide 17: How a CPU works?
still follows von Neumann model
A = B+C;
load R1, B; //R1 = mem[B];
load R2, C; //R2 = mem[C];
add R3, R1, R2; //R3 = R1+R2;
store A, R3; //mem[A] = R3;
A
B
C
memory

## Slide 18: How a CPU works?
still follows von Neumann model
A = B+C;
load R1, B; //R1 = mem[B];
load R2, C; //R2 = mem[C];
add R3, R1, R2; //R3 = R1+R2;
store A, R3; //mem[A] = R3;
A
B
C
memory

## Slide 19: 8051 Architecture Model

## Slide 20: Imagination on 8051 architecture
Imagine how data flow in the architecture!
R0
R1
R2
…
R7
general purpose
registers
A
B
P0
…
…
special function
registers (SFR)
ALU
8051 CPU core
…
…
address
30h
31h
32h
internal memory

## Slide 21: Imagination on 8051 architecture
flow of an arithmetic instruction
R0
R1
R2
…
R7
general purpose
registers
A
B
P0
…
…
special function
registers (SFR)
ALU
8051 CPU core
…
…
address
30h
31h
32h
internal memory

## Slide 22: Imagination on 8051 architecture
data movement between memory and registers
the MOV instruction
R0
R1
R2
…
R7
general purpose
registers
A
B
P0
…
…
special function
registers (SFR)
ALU
8051 CPU core
…
…
address
30h
31h
32h
internal memory

## Slide 23: Imagination on 8051 architecture
the MOV also for registers
R0
R1
R2
…
R7
general purpose
registers
A
B
P0
…
…
special function
registers (SFR)
ALU
8051 CPU core
…
…
address
30h
31h
32h
internal memory

## Slide 24: Imagination on 8051 architecture
Feature: most of instructions have limited use on registers
Example:
  ADD uses ACC
  MUL (multiply) uses A and B
R0
R1
R2
…
R7
general purpose
registers
A
B
P0
…
…
special function
registers (SFR)
ALU
8051 CPU core
…
…
address
30h
31h
32h
internal memory

## Slide 25: Special Function Registers (SFR)
accumulator
for multiply/divide
processor status word

## Slide 26: A first look on 8051 assembly program

## Slide 27: Features of 8051 CPU and assembly
8-bit data operation
two-operand assembly instruction
  Example: ADD A, R1 //A=A+R1

## Slide 28: Classification of instructions
Arithmetic (ADD, SUBB, MUL, etc.)
  Notice: the use of register
  e.g. ADD A, R0
  e.g. MUL AB
Branch (AJMP, ACALL, RET)
  Notice: the jump range
Data Transfer (MOV)
  direct/indirect addressing mode
Logical
  bit-addressible instruction

## Slide 29: 8051 assembly language looks like
[label:] mnemonic [operands] [;comment]
ORG 0H ;start (origin) at location 0 MOV R5,#25H ;load 25H into R5 MOV R7,#34H ;load 34H into R7 MOV A,#0 ;load 0 into A ADD A,R5 ;add contents of R5 to A ;now A = A + R5 ADD A,R7 ;add contents of R7 to A ;now A = A + R7 ADD A,#12H ;add to A value 12H ;now A = A + 12H
HERE: SJMP HERE ;stay in this loop END ;end of asm source file

## Slide 30: 8051 assembly language looks like
[label:] mnemonic [operands] [;comment]
ORG 0H ;start (origin) at location 0 MOV R5,#25H ;load 25H into R5 MOV R7,#34H ;load 34H into R7 MOV A,#0 ;load 0 into A ADD A,R5 ;add contents of R5 to A ;now A = A + R5 ADD A,R7 ;add contents of R7 to A ;now A = A + R7 ADD A,#12H ;add to A value 12H ;now A = A + 12H
HERE: SJMP HERE ;stay in this loop END ;end of asm source file
general form

## Slide 31: 8051 assembly language looks like
[label:] mnemonic [operands] [;comment]
ORG 0H ;start (origin) at location 0 MOV R5,#25H ;load 25H into R5 MOV R7,#34H ;load 34H into R7 MOV A,#0 ;load 0 into A ADD A,R5 ;add contents of R5 to A ;now A = A + R5 ADD A,R7 ;add contents of R7 to A ;now A = A + R7 ADD A,#12H ;add to A value 12H ;now A = A + 12H
HERE: SJMP HERE ;stay in this loop END ;end of asm source file
R7=0x34

## Slide 32: 8051 assembly language looks like
[label:] mnemonic [operands] [;comment]
ORG 0H ;start (origin) at location 0 MOV R5,#25H ;load 25H into R5 MOV R7,#34H ;load 34H into R7 MOV A,#0 ;load 0 into A ADD A,R5 ;add contents of R5 to A ;now A = A + R5 ADD A,R7 ;add contents of R7 to A ;now A = A + R7 ADD A,#12H ;add to A value 12H ;now A = A + 12H
HERE: SJMP HERE ;stay in this loop END ;end of asm source file
ACC=ACC+R5

## Slide 33: 8051 assembly language looks like
[label:] mnemonic [operands] [;comment]
ORG 0H ;start (origin) at location 0 MOV R5,#25H ;load 25H into R5 MOV R7,#34H ;load 34H into R7 MOV A,#0 ;load 0 into A ADD A,R5 ;add contents of R5 to A ;now A = A + R5 ADD A,R7 ;add contents of R7 to A ;now A = A + R7 ADD A,#12H ;add to A value 12H ;now A = A + 12H
HERE: SJMP HERE ;stay in this loop END ;end of asm source file
goto HERE

## Slide 34: Example 1: d=a*b+c

## Slide 35: In-Class Exercise
write the program d=a*b+c
  where a, b, c are originally in the memory
8051 instructions you need:
  add
  mul (multiplication)
  inc (increment)
  mov (move)
Check the instruction reference manual for restrictions on using register operands!

## Slide 36: Example: d=a*b+c
mov R1, #30h ; R1=30
mov A, @R1 ; A=mem[R1]
inc R1 ; R1++
mov B, @R1 ; B=mem[R1]
inc R1 ; R1++
mov R0, @R1 ; R0=mem[R1]=C
mul AB ;{A,B} = A*B
add A, R0 ; A=A+R0
wait:
sjmp wait
1
2
3
a
b
c

## Slide 37: Example: d=a*b+c
mov R1, #30h ; R1=30
mov A, @R1 ; A=mem[R1]
inc R1 ; R1++
mov B, @R1 ; B=mem[R1]
inc R1 ; R1++
mov R0, @R1 ; R0=mem[R1]=C
mul AB ;{A,B} = A*B
add A, R0 ; A=A+R0
wait:
sjmp wait
30h
1
2
3
a
b
c

## Slide 38: Example: d=a*b+c
mov R1, #30h ; R1=30
mov A, @R1 ; A=mem[R1]
inc R1 ; R1++
mov B, @R1 ; B=mem[R1]
inc R1 ; R1++
mov R0, @R1 ; R0=mem[R1]=C
mul AB ;{A,B} = A*B
add A, R0 ; A=A+R0
wait:
sjmp wait
30h
1
2
3
a
b
c

## Slide 39: Example: d=a*b+c
mov R1, #30h ; R1=30
mov A, @R1 ; A=mem[R1]
inc R1 ; R1++
mov B, @R1 ; B=mem[R1]
inc R1 ; R1++
mov R0, @R1 ; R0=mem[R1]=C
mul AB ;{A,B} = A*B
add A, R0 ; A=A+R0
wait:
sjmp wait
30h
1
2
3
a
b
c
1

## Slide 40: Example: d=a*b+c
mov R1, #30h ; R1=30
mov A, @R1 ; A=mem[R1]
inc R1 ; R1++
mov B, @R1 ; B=mem[R1]
inc R1 ; R1++
mov R0, @R1 ; R0=mem[R1]=C
mul AB ;{A,B} = A*B
add A, R0 ; A=A+R0
wait:
sjmp wait
30h
1
2
3
a
b
c
1

## Slide 41: Example: d=a*b+c
mov R1, #30h ; R1=30
mov A, @R1 ; A=mem[R1]
inc R1 ; R1++
mov B, @R1 ; B=mem[R1]
inc R1 ; R1++
mov R0, @R1 ; R0=mem[R1]=C
mul AB ;{A,B} = A*B
add A, R0 ; A=A+R0
wait:
sjmp wait
31h
1
2
3
a
b
c
1

## Slide 42: Example: d=a*b+c
mov R1, #30h ; R1=30
mov A, @R1 ; A=mem[R1]
inc R1 ; R1++
mov B, @R1 ; B=mem[R1]
inc R1 ; R1++
mov R0, @R1 ; R0=mem[R1]=C
mul AB ;{A,B} = A*B
add A, R0 ; A=A+R0
wait:
sjmp wait
31h
1
2
3
a
b
c
1
2

## Slide 43: Example: d=a*b+c
mov R1, #30h ; R1=30
mov A, @R1 ; A=mem[R1]
inc R1 ; R1++
mov B, @R1 ; B=mem[R1]
inc R1 ; R1++
mov R0, @R1 ; R0=mem[R1]=C
mul AB ;{A,B} = A*B
add A, R0 ; A=A+R0
wait:
sjmp wait
32h
1
2
3
a
b
c
1
2

## Slide 44: Example: d=a*b+c
mov R1, #30h ; R1=30
mov A, @R1 ; A=mem[R1]
inc R1 ; R1++
mov B, @R1 ; B=mem[R1]
inc R1 ; R1++
mov R0, @R1 ; R0=mem[R1]=C
mul AB ;{A,B} = A*B
add A, R0 ; A=A+R0
wait:
sjmp wait
32h
1
2
3
a
b
c
1
2
3

## Slide 45: Example: d=a*b+c
mov R1, #30h ; R1=30
mov A, @R1 ; A=mem[R1]
inc R1 ; R1++
mov B, @R1 ; B=mem[R1]
inc R1 ; R1++
mov R0, @R1 ; R0=mem[R1]=C
mul AB ;{A,B} = A*B
add A, R0 ; A=A+R0
wait:
sjmp wait
32h
1
2
3
a
b
c
1
2
3

## Slide 46: Example: d=a*b+c
mov R1, #30h ; R1=30
mov A, @R1 ; A=mem[R1]
inc R1 ; R1++
mov B, @R1 ; B=mem[R1]
inc R1 ; R1++
mov R0, @R1 ; R0=mem[R1]=C
mul AB ;{A,B} = A*B
add A, R0 ; A=A+R0
wait:
sjmp wait
32h
1
2
3
a
b
c
2
0
3

## Slide 47: Example: d=a*b+c
mov R1, #30h ; R1=30
mov A, @R1 ; A=mem[R1]
inc R1 ; R1++
mov B, @R1 ; B=mem[R1]
inc R1 ; R1++
mov R0, @R1 ; R0=mem[R1]=C
mul AB ;{A,B} = A*B
add A, R0 ; A=A+R0
wait:
sjmp wait
32h
1
2
3
a
b
c
2
0
3

## Slide 48: Example: d=a*b+c
mov R1, #30h ; R1=30
mov A, @R1 ; A=mem[R1]
inc R1 ; R1++
mov B, @R1 ; B=mem[R1]
inc R1 ; R1++
mov R0, @R1 ; R0=mem[R1]=C
mul AB ;{A,B} = A*B
add A, R0 ; A=A+R0
wait:
sjmp wait
32h
1
2
3
a
b
c
5
0
3

## Slide 49: Branch (Jump) Instruction

## Slide 50: What is a branch/jump instruction
the “goto” to control program execution path
add A, R1
sjmp label_1 ; goto label_1
mul AB
…
label_1:
add A, R2
the mul instruction won’t be executed

## Slide 51: Frequently used branch instructions of 8051
LJMP addr16 | Long jump | 3 | 4
SJMP rel | Short jump (from –128 to +127 locations relative to the following instruction) | 2 | 3
JC rel | Jump if carry flag is set. Short jump. | 2 | 3
JNC rel | Jump if carry flag is not set. Short jump. | 2 | 3
JB bit,rel | Jump if direct bit is set. Short jump. | 3 | 4
JBC bit,rel | Jump if direct bit is set and clears bit. Short jump. | 3 | 4
JMP @A+DPTR | Jump indirect relative to the DPTR | 1 | 2
JZ rel | Jump if the accumulator is zero. Short jump. | 2 | 3
JNZ rel | Jump if the accumulator is not zero. Short jump. | 2 | 3
for more, check http://www.mikroe.com/en/books/8051book/ch3/

## Slide 52: Conditional Branch Instructions
JC: Jump if Carry=1
JNC: Jump if Carry=0
JZ: Jump if A=0
JNZ: Jump if A!=0
DJNZ Rn, location
  Rn = Rn-1
  jump if Rn!=0

## Slide 53: How conditional branch works in 8051?
an arithmetic instruction sets bits in PSW
the conditional branch checks bits in PSW to determine whether to jump or not

## Slide 54: How conditional branch works in 8051?
an arithmetic instruction sets bits in PSW
the conditional branch checks bits in PSW to determine whether to jump or not
a register in SFR

## Slide 55: How conditional branch works in 8051?
an arithmetic instruction sets bits in PSW
the conditional branch checks bits in PSW to determine whether to jump or not
carry flag set by ALU
ALU
D1
D0
out
carry
11011010
11101011
+)
11000101
1
carry

## Slide 56: Example of conditional branch instruction
JC label
  if (C==1) goto label
JNC label
  if (C==0) goto label

## Slide 57: In-Class Exercise
write the program:
if (R0+R1>0xff)
A = 0xff;
else
A = R0+R1

## Slide 58: Example: using JNC
if (R0+R1>0xff)
A = 0xff;
else
A = R0+R1
A = R0;
A = A+R1; //implicitly set C
if (C==0) goto exit;
A = 0xff;
exit:
…
mov A, R0
add A, R1
JNC exit
mov A, #ffh
exit:
…

## Slide 59: Example: a simple for loop

## Slide 60: A useful instruction
DJNZ Rn, location
  Rn = Rn-1
  jump if Rn!=0

## Slide 61: Loop example
sum = 0;
for (i=10;i>0;i--)
sum = sum+i;
A = 0; //A is sum
R0 = 10; //R0 is i
loop_start:
A = A+R0;
if (--R0) goto loop_start;
mov A, #0
mov R0, #10
loop_start:
add A, R0
djnz R0, loop_start

## Slide 62: Now you should be able to do your work
write a program to compute
  where A[i], B[i] are integer array (8-bit) in 8051’s internal memory
instructions you may use:
  ADD (addition)
  MUL (multiply)
  MOV (move data)
  DJNZ (decrement and jump if not zero)
Check the instruction reference manual!

## Slide 63: How to build an executable program
Recap on the system programming before the practical guide

## Slide 64: The Next Lab: LED lights