## Slide 1: Sound Control
Lab 07

## Slide 2: Your Task
Play a song you like
  multiple tones
  frequency of sound changes regularly

## Slide 3: Pre-Lab Report
Q1: Briefly describe the clock system of C8051F040
  Check the data sheet
Q2: How to generate a clock signal with 100Hz frequency in C8051F040
  Specify the setup of OSICN, CLKSEL, TMOD, TCON, THx, TLx, etc.

## Slide 4: Grading Policy
Basic (70%): play each tone by request
  Do, Re, Mi, Fa, So, La, Si, Do
Play a song (+10%)
  歌譜 stored in an array and can be changed without modifying the program
Show the time-counting on LCD/GLCD while the song is playing (+10%)
  three jobs controlled by timers
  using 3 timers?
Your Report: 10%

## Slide 5: Things you will learn today
Control everything by timer interrupts

## Slide 6: Outline
How to control the buzzer (蜂鳴器) to play required sound?
How to generate a signal with required frequency?
  play a sound with fixed frequency
How to play a song?
  the frequency changes with time
time
A
A
B
B
B
C
C
C
C
C
C
C
A
B
C
periodic tasks

## Slide 7: How to control the buzzer

## Slide 8: How to control the buzzer
control the sound by the frequency f of the input signal to the buzzer
time
…
1 sec
f = number of pulses in one second

## Slide 9: Appendix: frequency of tones

## Slide 10: Generating a signal with given frequency

## Slide 11: How to send out regular pulses with given frequency
It’s difficult to fine-tune delay count N to match T/2 (if you use a for-loop)
This method is not recommended!
main () {
while (1) {
status = ~status;
P2.7 = status;
delay (N);
}
}
time
…
1 sec
T

## Slide 12: The Problem
Frequency generation using timer interrupt
  Suppose: the period for timer interrupt is 100us
  Question: How to generate a signal with half-period n*100us ?
time
P1.0
100 us
n*100 us

## Slide 13: The method
just reverse the signal every n times the timer ISR is called
time
P1.0
100 us
n*100 us
int n;
int count=0;
char status;
Timer_ISR ()
{
count = (count+1)%n;
status=~status;
if (count==0) P2.7 = ~status;
}
n times

## Slide 14: How to play a song?
the frequency changes with time

## Slide 15: The method
Store the 歌譜 as an array of half-period
  Song_Table[i] = the half-period of the i-th tone
Use two timer interrupts
  Timer0_ISR: to control the signal frequency by half-period n
  Timer1_ISR: change the half-period (n) periodically
    n = Song_Table[i++]

## Slide 16: The method
int Song_Table[3];
main ()
{
//setup timer interrupts
//initialize
Song_Table [0] = Half_Period (Do);
Song_Table [1] = Half_Period (Re);
Song_Table [2] = Half_Period (Mi);
…
while (1) P2.7=status;
}
int n;
int count;
char status;
Timer0_ISR () //to control signal frequency
{
count = (count+1)%n;
if (count==0) status=~status;
}
int i;
Timer1_ISR () //to change the tone
{
//counting for 1 second…
n = Song_Table [i];
i = (i+1)%3;
}

## Slide 17: The method
int Song_Table[3];
main ()
{
//setup timer interrupts
//initialize
Song_Table [0] = Half_Period (Do);
Song_Table [1] = Half_Period (Re);
Song_Table [2] = Half_Period (Mi);
…
while (1) P2.7=status;
}
int n;
int count;
char status;
Timer0_ISR () //to control signal frequency
{
count = (count+1)%n;
if (count==0) status=~status;
}
int i;
Timer1_ISR () //to change the tone
{
//counting for 1 second…
n = Song_Table [i];
i = (i+1)%3;
}
Half period of each tone is stored in an array

## Slide 18: The method
Frequency generator according to half-period n
int Song_Table[3];
main ()
{
//setup timer interrupts
//initialize
Song_Table [0] = Half_Period (Do);
Song_Table [1] = Half_Period (Re);
Song_Table [2] = Half_Period (Mi);
…
while (1) P2.7=status;
}
int n;
int count;
char status;
Timer0_ISR () //to control signal frequency
{
count = (count+1)%n;
if (count==0) status=~status;
}
int i;
Timer1_ISR () //to change the tone
{
//counting for 1 second…
n = Song_Table [i];
i = (i+1)%3;
}

## Slide 19: The method
int Song_Table[3];
main ()
{
//setup timer interrupts
//initialize
Song_Table [0] = Half_Period (Do);
Song_Table [1] = Half_Period (Re);
Song_Table [2] = Half_Period (Mi);
…
while (1) P2.7=status;
}
int n;
int count;
char status;
Timer0_ISR () //to control signal frequency
{
count = (count+1)%n;
if (count==0) status=~status;
}
int i;
Timer1_ISR () //to change the tone
{
//counting for 1 second…
n = Song_Table [i];
i = (i+1)%3;
}
Frequency generator according to half-period n
changes half-period n of the generated signal every second