## Slide 1: Mid-Term Project
Multi-Function Digital Watch

## Slide 2: Basic: Digital Clock (50%)
Clock Mode :
  display time hh:mm:ss and refresh every second
A “Mode Button” to change to other functionality
  Such as “Calculator Mode”
Calculator Mode
Clock
hh:mm:ss
Clock Mode
Mode Button

## Slide 3: Basic Calculator Mode(+10%)
Calculator Mode :
  basic compute for 8-bit number(127~-128)
    Input : 12 + 65 = , Output : 77
    Input : 12 – 65 = , Output : -53
    Input : 21 x 3 = , Output : 63
    Input : 21 / 3 = , Output : 7
    Input : 20 / 3 = , Output : 6
12+65=
77
Calculator Mode
12+65=
Calculator Mode
Mode Button

## Slide 4: Bonus at Calculator Mode
Compute for 32-bit number
  Addition and Subtraction for 32-bit (+10%)
    1234567890+123456789=1358024679
  Multiplication for 32-bit (+10%)
  Division for 32-bit (+15%)
1234567890+123456789=1358024679
Calculator Mode
1234567890+123456789=
Calculator Mode
Mode Button

## Slide 5: Bonus at Calculator Mode
Engineering Calculator(+15%)
  1 + 2 x 3 = 7
  28 / 4 + 9 x 3 – 2 x 3 x 3 = 16
28/ 4+9x3–2x3x3=
16
Calculator Mode
28/ 4+9x3–2x3x3=
Calculator Mode
Mode Button

## Slide 6: Bonus at Calculator Mode (+15%)
Arithmetic Question Provider
  LCD顯示算術題目。
  由Buttons輸入答案。
  按下Send Button送出答案。
  輸入答案正確分數加一分，並由LCD顯示目前總分。
  輸入答案錯誤分數不變，並由LCD顯示目前總分。
  總共20題，前5題回答時間為3秒，中間10題回答時間為2秒，最後5題回答時間為1秒。
  回答時，LED燈由高亮到低。
123+111=
Arithmetic Mode
Mode Button
Correct
Score : 1
Arithmetic Mode
Send Button
Input 234

## Slide 7: Alarm Mode
Press “Mode” button to set the alarm time (+10%)
  One digit each time
  Press “number” to set current digit
  Press “Mode” button to switch to the next digit
  Turn back to Clock Mode after the last digit been set
Blink on the digit been set (+10%)
Show alarm by some running LED pattern (+5%)
Show alarm by “running text” on LCD (+10%)